## Slide 1: Airborne Compact Raman Lidar (CRL) Data Collection during PECAN
Zhien Wang (zwang@uwyo.edu), Decheng Wu, Bart Geerts, Min Deng, and King Air team
University of Wyoming

## Slide 2: University of Wyoming King Air Instrumentation
Compact Raman lidar (CRL, nadir): aerosol (LSR), water vapor and temperature
Wyoming Cloud Lidar (WCL, zenith): aerosol
In situ measurements
  PCASP: Aerosol size distribution
  Wind
  Water vapor, state variables
  pressure perturbations (differential GPS)

## Slide 3: Compact Raman Lidar (CRL)
12 inch telescope
Laser: 50 mJ at 30 Hz
Added a Raman temperature channel for PECAN
Optimized for nighttime operations
The new five channel receiver
12x18x5 inches
CRL is a prototype for MARLi

## Slide 4: Data Processing
Calibrations: In situ measurements from designated flight patterns
Short-range overlap corrections:
  Using clear sky for aerosol channels
  Using stacked legs for water vapor and temperature channels
An example of determining overlap correction factor g(z) for temperature measurements based on measurements at ~3.1 km and ~2.5 km legs.
Wu et al., OE, 2016, A1210-A1223

## Slide 5: Averaging and noise
uncertainties that arise from random noise in the lidar signals using different horizontal (Δx) and vertical (Δz) filters.
Raw data resolution:
  Dz ~ 0.6 m
  Dx ~ 20-100 m
Averaging to suppress random noise.

## Slide 6: Averaging and Noise
best-estimate temperature
calibration uncertainty
noise uncertainty
100 km

## Slide 7: Data Availability and Issues
No CRL temperature estimates before June 15.
  due to an impedance mismatch issue (PMT)
One water vapor calibration coefficient was used for whole campaign.
Noise increases with range: CRL measurements beyond 2 km are noisy – requiring coarser averaging.

## Slide 8: Combined WCL and CRL Measurements
qv
T
aerosol
Depolarization
2 July 2015

## Slide 9: CRL and LASE: water vapor comparison
CRL and LASE agree well; CRL reveals fine scale structures.
CRL
LASE
12 July 2015
FP1
FP3
FP2

## Slide 10: An Example of CRL Measurements
Water Vapor
Aerosol
Temperature
King Air sampling MCS inflow July 1, 2015

## Slide 11: a zoom-in near the edge of cold pool
qv
T
aerosol
inbound leg
outbound leg
Notes: bore or gust front?

## Slide 12: Convective Initiation
02:21
June 8, 2015
north
south
Notes: Legs:
0-2:11
1-2:22
2-2:25
3-2:30
4-2:36
5-2:46

## Slide 13: Convective Initiation
02:46
June 8, 2015
south side
Notes: Legs:
0-2:11
1-2:22
2-2:25
3-2:30
4-2:36
5-2:46

## Slide 14: Convective Initiation
02:46
June 8, 2015
north
south
Notes: Legs:
0-2:11
1-2:22
2-2:25
3-2:30
4-2:36
5-2:46

## Slide 15: Convective Initiation
02:46
June 8, 2015
north
south
Notes: Legs:
0-2:11
1-2:22
2-2:25
3-2:30
4-2:36
5-2:46

## Slide 16: Multi-function Airborne Raman Lidar (MARLi)
Finished more than 40-hr testing flight on C-130 and King Air in summer, 2016

## Slide 17: Coastal Atmospheric Boundary Layer Structure
California coast around Shelter Cove
Vertical sawtooth profiling to compare with in situ probes.
Different level legs for MARLi profiling
UWKA

## Slide 18: Comparison of Spatial Temperature Structure from in situ and MARLi
06/30/2016

## Slide 19
qv
T
aerosol
Depolarization
marine BL (optically clear)
06/30/2016
Notes: LSR (the ratio of total backscattering to molecular backscattering) represents aerosol loading.
Aerosol Dep shows sea salt crystallization and mixing.

## Slide 20: Fine-scale Water Vapor and temperature Structure above the Stratocumulus Cloud Top
Water Vapor
Aerosol/Cloud
Temperature
Cloud top
Notes: The entrainment or mixing over stratocumulus cloud top is an important processes controlling cloud evolution. But the process is difficult to observe and poorly simulated in models.
MARLi example give above highlight the new measurement capability to provide fine scale temperature and water vapor measurements to visualize related processes.

## Slide 21: Summary
CRL together with other King Air instruments offer a powerful dataset to study atmospheric boundary layer structure around storms.
If you have any special request, let us know.
MARLi is ready for deployments on UWKA and C-130.
Check out Guo Lin’s poster for more CRL measurements