## Slide 1: Current State of Processing of the PECAN Microphysics Dataset
Greg M. McFarquhar1, Daniel M. Stechman1, Robert M. Rauber1, Robert A. Black2 and Brian F. Jewett1
1University of Illinois at Urbana-Champaign, Urbana, IL
2National Oceanic and Atmospheric Administration – Hurricane Research Division, Miami, FL

## Slide 2
Instrumentation: Imaging Probes
Cloud Imaging Probe (CIP)
64 laser diodes with 25 µm resolution
  (~125 µm to 1600 µm)
Good quality data
Precipitation Imaging Probe (PIP)
64 laser diodes with 100 µm resolution
  (~0.6 mm to 6.4 mm)
Data quality not as good, but some data recoverable
Notes: 150 um chosen as lower bound because there are many uncertainties concerning the validity of particles smaller than this
e.g., Shattered particles
PIP probe was also used, though there were lots of fogging problems.
We’re carefully assessing the reliability of this data and working to incorporate it into future analyses.

## Slide 3
Instrumentation: Droplet Probes
Cloud Droplet Probe (CDP)
Size measured by forward scattering of light (2 mm to 50 mm)
Cloud Aerosol Spectrometer (CAS)
Size measured by forward scattering of light
  (0.53 to 50 mm)
These data can be trusted for liquid droplets
Notes: 150 um chosen as lower bound because there are many uncertainties concerning the validity of particles smaller than this
e.g., Shattered particles
PIP probe was also used, though there were lots of fogging problems.
We’re carefully assessing the reliability of this data and working to incorporate it into future analyses.

## Slide 4
Instrumentation: Hot Wire Probes
SEA hot-wire probe
Directly measures LWC
  0-10 g/m3 for airspeeds < 150 m/s
Notes: 150 um chosen as lower bound because there are many uncertainties concerning the validity of particles smaller than this
e.g., Shattered particles
PIP probe was also used, though there were lots of fogging problems.
We’re carefully assessing the reliability of this data and working to incorporate it into future analyses.

## Slide 5: Processing Optical Array Probe Data
Three primary steps in UIOPS:
Process raw binary image data, and convert to netCDF
Reject particles & determine morphology of each particle
Calculate 1-second particle size distributions (PSDs) and bulk microphysical quantities
Use UIOPS (University of Illinois Optical Array Probe Processing Software)

## Slide 6: Quality Control
Following particles are rejected:
Shattered artifacts
  Short interarrival time suggests shattered artifact
Out of focus particles
  Often yields “hollow” particles due to probe depth of field limitations
“Streakers” and stuck bits

## Slide 7: Calculated Quantities
Particle-by-Particle Properties
Maximum dimension
Projected area
Aspect ratio
Area ratio
Estimated mass
Identified habit
Size Distribution Bulk Properties
Total number concentration
Total extinction
Total ice water content
Total reflectivity
Effective radius
Median mass dimension
Mass-weighted terminal velocity
Precipitation rate

## Slide 8: Size Distribution Data
1-sec averages for archived data
We suggest using at least 5-sec average for statistical significance

## Slide 9
Total Number Concentration

## Slide 10: Mass Distribution Functions
Need PIP data for a complete analysis

## Slide 11: PIP Data Quality
Fogging and/or icing caused data quality issues and at times complete failure of PIP
Good Data (CIP)
Partially Corrupt Data (PIP)

## Slide 12: PIP Data Quality
We will be analyzing the PIP data on a second-by-second basis to determine which periods contain usable data

## Slide 13: CAS Probe

## Slide 14: Representative Particle Images
Images of all particles will be available on archive as function of time
For spirals, we will generate plots showing selected images binned by temperature

## Slide 15: PECAN Spirals
20150617 - IOP 11 |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | ! | ! | !
2 | P | P | P | ! | ! | !
3 | P | P | P | ! | ! | !
4 | P | P | P | ! | ! | !
5 | P | P | P | ! | ! | !
6 | P | P | P | ! | ! | !
7 | P | P | P | ! | ! | !
20150620 - UFO 4 |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | ! | ! | !
2 | P | P | P | ! | ! | !
3 | P | P | P | ! | ! | !
4 | P | P | P | ! | ! | !
5 | P | P | P | ! | ! | !
6 | P | P | P | ! | ! | !
20150701 – IOP 17 |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | ! | ! | !
20150702 – UFO 8A |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | X | X | X
2 | P | P | P | X | X | X
3 | P | P | P | X | X | X
20150706 - IOP 20 |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | ! | ! | !
2 | P | P | P | ! | ! | !
3 | P | P | P | ! | ! | !
4 | P | P | P | ! | ! | !
5 | P | P | P | ! | ! | !
6 | P | P | P | ! | ! | !
7 | P | P | P | ! | ! | !
20150709 - IOP 21 |  |  |  |  |  | 
Spiral # | CIP PbP Data | CIP SD Data | CIP Rep. Particle Plot | PIP PbP Data | PIP SD Data | PIP Rep. Particle Plot
1 | P | P | P | ! | ! | !
2 | P | P | P | ! | ! | !
3 | P | P | P | ! | ! | !
4 | P | P | P | ! | ! | !
5 | P | P | P | ! | ! | !
6 | P | P | P | ! | ! | !
7 | P | P | P | ! | ! | !
8 | P | P | P | ! | ! | !
9 | P | P | P | ! | ! | !
10 | P | P | P | ! | ! | !
11 | P | P | P | ! | ! | !
12 | P | P | P | ! | ! | !
13 | P | P | P | ! | ! | !
14 | P | P | P | ! | ! | !
15 | P | P | P | ! | ! | !
16 | P | P | P | ! | ! | !
**No spirals during IOP 25, UFO 12, and IOP 27**
P | P | ! | X
Complete – Ready for Archive | Ready to Produce | Incomplete – Pending PIP QC | No Data

## Slide 16: Archival
We will begin uploading QC’d data to the archive soon
(will be assigned a DOI)
Ready for upload to the data archive:
CIP particle-by-particle and size distribution data
Select representative particle image plots
Not currently on the archive (obtained from NOAA HRD)
Should they be on archive?
No/limited processing:
PIP particle-by-particle and size distribution data
SEA, CAS, and CDP data
Raw CIP/PIP data

## Slide 17: Archival
Encourage collaborative use of the data
Looking for friendly users to use data in their investigations
 Contact Greg McFarquhar if interested
mcfarq@illinois.edu